Vedran Brnjetic, Oheneba, Thanh, GeonHui Yoon (Jamie)
07.11.2017
The Zumo Robot was given along with the rechargeable batteries (1.4V*4).
The voltage of the batteries was calculated.
The voltage which was scaled down (3.8V) was multiplied by the scale factor which is 2/3, giving the actual battery voltage reading which was 5.18V.

08.11.2017
The Zumo Robot was programmed to run along the test tracks.

First, a delay was given after the robot was set on the starting line of the track with

motor_forward(0, 3000);	where 0=speed
3000=time in milliseconds

Along the first line, the robot was programmed to travel straight with

motor_forward(100, 5600);

The robot then took a 90-degree turn to the right with

motor_turn(200, 0, 358);	(s of left motor, s of right motor, time)
(this speeds up the left motor, stops the right motor for turning)
The robot then proceeded to go along the second line with

motor_forward(100, 4180);

The robot took another 90-degree turn to the right with

motor_turn(200, 0, 370);

The robot continued along the third line with

motor_forward(100, 5580);,

bringing the robot to a sharp turn which was achieved with

motor_turn(200, 0, 690);.

Then, the robot continued along the smooth curve with

motor_turn(40, 60, 12200);

Finally, the robot was brought to the finishing line.

Update by Vedran, after a few successful runs, a problem appeared yesterday with the motors. Forward drive no longer works as expected. I suspect hardware malfunction – something blocking it. Probably dust. I reprogrammed it yesterday to go backwards the same track which proved to be a success. However, once we run with sensors this will be a problem. Suggest talking to Joe or Keijo to get it fixed, cleaned or the robot replaced.

15.11.2017
We cross-checked the values of the sensor once more since we were more used to using the dig values which are straightforward. We played around with the alternate code for following the line. For the sensor readings we normally use the “dig” values but we decided to test the “ref”/ analog values and they weren’t great, so we reverted to the “dig” values. In general, we revised our code and tested two different approaches to know the better of the two.